## Slide 1: Model-driven Software Engineering for Connected Vehicles
Embedded Monti Arc (EMA)
Ahmed, Ana, Andreas, Anja, Lukas, Martin, Mattis
Advisor: Evgeny Kusmenko
Lab
Chair of Software Engineering
RWTH Aachen University

## Slide 2: EmbeddedMontiArc Family
A C&C modeling language family
New textual approach for modeling
It includes
  An architecture description language
    subdividing a system into its components and sub-components (EmbeddedMontiArc),
  A mathematical matrix-based behavior modeling language (MontiMath),
  A stream language for model-based testing (Stream), etc.

## Slide 3: EmbeddedMontiArcMath Langauge
A combination of EmbeddedMontiArc and MontiMath languages
component SensorFusion <N1 n> (Q^{1,n} (-90°:90° tilt=zeros(1,n))){
ports
in Q(0m:0.2m:10m) distance[n];
out Q(0m:0.2m:10m) mergedDistance;
implementation Math{
diag Q (0:1) ^{n,n} facMatrix = diag(cos*(tilt));
mergedDistance = min(distance * facMatrix);
}
}
EMAM
Source: “Modeling Architectures of Cyber-Physical Systems”, Kusmenko, Roth, Rumpe,von Wenckstern

## Slide 4: Requirement Template
ID | Name | 
REQ-10 | Rerouting | 
Description |  | 
Upon encountering a blockage in a road or receiving a signal from another vehicle that there’s in a traffic jam (REQ-7), the vehicle should be able to change its trajectory avoiding that road and still reaching its destination. |  | 
Type | Dependencies | Approved
FR | REQ-7 | ✓
Function requirement (FR)
Non-functional requirement (NFR)
Mechanical requirement
...
Approved by the client?

## Slide 5: Requirements
Fulfilled:
Following a path
Lane keeping
Upper speed limit sensors
Comfortable acceleration and steering
Battery level sensor
Object detection sensor
Next steps:
Respecting the upper speed limit
Safety distance
Collision avoidance
Intersection handling
  signalized and unsignalized
Platooning

## Slide 6: Architecture
Autopilot
EMA
Movement
Communication
Behaviour
Navigation
Environment

## Slide 7: Architecture
Autopilot
EMA
Movement
Communication
Behaviour
Navigation
ComInputs
C2C_Info
ComOutputs
Environment

## Slide 8: Architecture
Autopilot
EMA
Movement
Communication
Behaviour
Environment
Navigation
ComInputs
C2C_Info
ComOutputs
WeatherInfo
WeatherInfo

## Slide 9: Architecture
Autopilot
EMA
Movement
Communication
Behaviour
Environment
Navigation
ComInputs
C2C_Info
ComOutputs
WeatherInfo
TempoLimit
WeatherInfo
BehaviourInfo

## Slide 10: Architecture
Autopilot
EMA
Movement
Communication
Behaviour
Environment
Navigation
ComInputs
C2C_Info
ComOutputs
CarInfo
HighLvlNav
PathInfo
WeatherInfo
TempoLimit
WeatherInfo
BehaviourInfo

## Slide 11: Architecture
Autopilot
EMA
Movement
Communication
Behaviour
Environment
Navigation
set_gas
set_steering
set_braking
ComInputs
C2C_Info
ComOutputs
CarInfo
HighLvlNav
PathInfo
WeatherInfo
TempoLimit
WeatherInfo
BehaviourInfo

## Slide 12: Architecture
PID
Driving Profile

## Slide 13: Car 2 Car Communication – General Information
Design and Implementation with standardized protocol
Communication with packets over sockets
General Information packet (StatePacket)
Other packets based on real-world scenarios
Optional „Authority“-flag
VehicleCommunication
EMA
Packets
Scenarios
1:n
n:1
Helpers
m:n
Notes: Designed protocol for standardized communication between the cars
Communication done via Sockets and encapsuled in a state and scenario depending packets
Cars can communicate with all other cars in transmission-range, directly or via broadcast
StatePacket transmitted via broadcast at all times
Scenario depending packets were designed on real-world scenarios -> platooning, battery-charge, traffic-jam and many more
Optional authority flag for police/emergency cars
Arch: main component is VehicleCommunication Component
VehicleCom has N scenarios; every scenario can utilize a packet and an arbitrary number of helpers

## Slide 14: Car 2 Car Communication – Platooning
Platoon access:
  Leadership handover
  Non-leading cars follow and synchronize with leader
  Join Requests, leading car decision
  Leave platoon any time
Other features:
  Negotiate waiting or gathering point
  Request battery charging if destination not reachable
  Leader signals platoon that destination was reached
Notes: Cars can form platoons, one car takes leadership and manages who can join
The non leading cars try to synchronize the movements of the leading car -> only if secure action atm
Cars can request to join and leave at any time
If cars get delayed (accident, sudden road blockade) they can request the platoon to wait; leader can decide if platoon waits on the spot or calculate a gathering point with position of platoon and position of delayed cars to meet up
When platoon reaches destination leading car can inform other cars and initiate search for parking spots

## Slide 15: Car 2 Car Communication – Flow of Communication (Emergency Braking)
:Car1
Broadcast(StatePacket)
:Car2
Broadcast(StateUpdated)
Broadcast(SafetyDistanceUpdated)
SD
:Car3
Distance and Direction
Calculation
Broadcast(StatePacket)
Broadcast(StateUpdated)
Brake
Broadcast(StatePacket)
Broadcast(StateUpdated)
Broadcast(StatePacket)
Broadcast(StateUpdated)
bi-directional communication
Broadcast(SafetyDistancePacket)
Notes: 3 Cars; all broadcasting their state; StatePacket ->Position,Velocity and Heading of car; StateUpdated -> signal that package was updated in current tick
Car3 calculates based on position difference that Car2 is too close and initiates braking
Car3 Broadcasts SafetyDistancePacket which announces the action and informs other cars about target velocity so they might brake to avoid the safety violation
After successful regulation of distance all cars resume broadcasting the StatePacket

## Slide 16: Sensors
Todo:
  Traffic Light Sensor
  Weather Sensor (temperature + humidity)
Implemented:
  LiDAR / Object Detection Sensor
  Speed Limit Sensor
  Battery Sensor
Existing:
  TrueCompass
  TruePosition
  TrueVelocity

## Slide 17: LiDAR / Object Detection
2 distance sensors for each direction
labeled with „front_left_lidar“, „back_left_lidar“, …
front
8.43m
8.40m
200m
200m
1.15m
1.12m
1.5m
1.49m

## Slide 18: Speed Limit Sensor
double[] trajectoryX = {90.24, 102.53, 108.46, 111.12 , ...}
double[] trajectoryY = {40.56, 44.92 , 41.42 , 46.94 , ...}
(90.24,40.56)
(102.53,44.92)
(108.46,41.42)
(111.12,46.94)
double[] upper_speed_limit = {50,50,30,…}
50 km/h
30 km/h
50 km/h

## Slide 19: Test Scenarios
57 test cases total
26 implemented as json scenarios

## Slide 20: Test Scenarios
Test ID | TC-2.1.1 | Requirement | REQ-2.1
Pre Conditions | Upper speed limit sensor exists |  | 
Description | Check vehicle response when it drives on a road with a speed limit of 50km/h. |  | 
Test Steps | 1. Place vehicle on any road of the map 2. Set a path that contains a road with a speed limit of 50 km/h. 3. Run scenario. |  | 
Expected Result | The vehicle starts driving. While driving on the road with the 50km/h speed limit, the car should have a speed between 45 km/h and 50 km/h. |  | 

## Slide 21: Demo

## Slide 22: Summary
EMA:
  Compiler error messages not expressive enough
  CoCos need to be enabled/extended
Requirements:
  Designed beyond scope of this lab
  Easily extensible
Architecture:
  Highly Modular
  High cohesion and low coupling
Car 2 Car Communication:
  Challenging implementation process
  EMA and Simulator incompatibility issues

## Slide 23: Summary
Sensors:
  LiDAR Sensor and Speed-limit Sensor implemented
  Missing data from simulator for other sensors
Tests-Scenarios:
  Several test cases for each requirement
  Not all implemented due to limitations of simulator
Outlook:
  More features with simulator extension
  Requirements and scenarios designed, implementation next
  EMA actively developed