Scenarios / Use-Cases

ID:	SCE-
Name:
Created:		Last Updated:
Description:
Actors:
Preconditions:
Postconditions:
Flow:
Alternative Flows:
Exceptions:
Requirements:
Test Cases:

ID:	SCE-1
Name:	Transportation from current position to target destination
Created:	28.11.2020	Last Updated:	28.11.2020
Description:	The user enters a destination and the vehicle will transport him to the destination.
Actors:	User, Autopilot
Preconditions:
Postconditions:
Flow:	User enters a destination and starts the vehicle. / Autopilot computes the optimal path from the current position to the destination / Autopilot safely drives the vehicle to the destination
Alternative Flow 1	User enters a path instead of a destination / Autopilot will compute the optimal way from the current position to the starting point of the given path / Autopilot safely drives the vehicle along the path to the destination
Alternative flow 2	The vehicle will display an error if the destination or a point of the path cannot be found or reached.
Requirements:	All
Test Cases	All

ID:	SCE-2
Name:	Manual Speed control
Created:	28.11.2020	Last Updated:	28.11.2020
Description:	The user changes the speed of the vehicle while driving
Actors:	User, Autopilot
Preconditions:	The vehicle is currently driving on a path to its destination.
Postconditions:
Flow:	User enters the desired speed / Vehicle checks the local speed limit / Vehicle changes the speed to desired value
Alternative Flows:	Vehicle displays an error message if the desired speed is higher than the local top speed limit or lower than the local bottom speed limit
Exceptions:
Requirements:	REQ 2
Test Cases	TC-2.2.*

ID:	SCE-3
Name:	Regenerative braking
Created:	28.11.2020	Last updated	28.11.2020
Description:	When stopping the vehicle, the vehicle converts the kinetic energy into a form that can be stored for later use, thus charging the battery
Actors:	User, Autopilot
Preconditions:	The vehicle is braking
Postconditions:	The battery is recharged (if sufficient amount of energy is stored)
Flow:	The vehicle starts braking / The vehicle slows down / The battery is charged
Alternative Flows:	The battery is not recharged when insufficient amount of energy is generated
Exceptions:
Requirements:	REQ-3.1, REQ-12
Test Cases	TC-3.1.1, TC-12.1.1, TC-13.1.1

ID:	SCE-4a
Name:	Collision Avoidance
Created:	28.11.2020	Last Updated:	28.11.2020
Description:	The vehicle recognizes and avoids other vehicles and obstacles
Actors:	Autopilot, Other vehicle
Preconditions:	The vehicle is currently driving on a path to its destination.
Postconditions:
Flow:	Sensors detect a different vehicle in front / Vehicle keeps a safety distance to the other vehicle and follows it at the same speed until their paths separate
Alternative Flows:	Sensors detect an obstacle (immovable object that is in the path of the vehicle) / Vehicle slows down and comes to a halt before the obstacle. If the vehicle is too close to the obstacle, emergency braking is triggered
Exceptions:
Requirements:	REQ-3
Test Cases:	TC-3.1.*, TC-3.2.*, TC-3.3.*, TC-3.4.*

ID:	SCE-5
Name:	Unsignalized Intersection Handling
Created:	28.11.2020	Last Updated:	28.11.2020
Description:	The autopilot approaches an unsignalized intersection and acts according to the local road traffic laws.
Actors:	Autopilot , Other vehicles
Preconditions:	The vehicle is driving along a path and reaching an intersection
Postconditions:
Flow:	Autopilot stops at the intersection / Autopilot checks if there are any other vehicles coming from one of the other entrances / Autopilot continues on its way through the intersection
Alternative Flows:	Autopilot recognizes that other vehicle(s) has/have the way of right / Autopilot waits until the other vehicle(s) has/have crossed the intersection / Autopilot continues on its way through the intersection
Exceptions:
Requirements:	REQ-3.2, REQ-6.1
Test Cases:	TC-6.1.*

ID:	SCE-6
Name:	Signalized Intersection Handling
Created:	28.11.2020	Last Updated:	28.11.2020
Description:	The vehicle approaches a signalized intersection and acts according to the local road traffic laws.
Actors:	Autopilot , Other vehicles, Traffic Light
Preconditions:	The vehicle is driving along a path and reaching an intersection
Postconditions:
Flow:	Autopilot detects the current status of the traffic light / Traffic light is green / Autopilot wants to turn left (right) so it checks if there is incoming traffic / Autopilot waits for incoming traffic to pass through / Autopilot turns left (right) at the intersection
Alternative Flows:	Green traffic light: / Autopilot wants to continue straight or turn right / Autopilot continues along its path / Yellow traffic light: / Autopilot checks distance to intersection / Autopilot slows down and comes to a halt before the intersection if the braking distance allows it otherwise it continues / Autopilot waits for the light to turn green again / Red traffic light: / Autopilot slows down and comes to a halt before the intersection / Autopilot waits for the light to turn green again
Exceptions:
Requirements:	REQ-6.1, REQ-6.2
Test Cases:	TC-6.1.*, TC-6.2.*

ID:	SCE-7
Name:	Emergency braking
Created:	28.11.2020	Last Updated:	28.11.2020
Description:	Maximum brake force is applied
Actors:	Autopilot
Preconditions:	The vehicle is going over a certain threshold between an obstacle and itself which implies immediate danger, if the vehicle doesn’t stop
Postconditions:
Flow:	The vehicle is driving on it’s path at a certain speed / The sensors detect an obstacle / The distance to the obstacle is calculated to be too little / Emergency braking is triggered
Alternative Flows:	When the obstacle is too small like a small stick or a small pile of leaves, the vehicle does not ingage emergency braking.
Exceptions:
Requirements:	REQ-3.1, REQ 3.2
Test Cases:	TC-3.5.1

ID:	SCE-8
Name:	Traffic jam detection
Created:	28.11.2020	Last updated:	28.11.2020
Description:	The vehicle sends a signal and position to other nearby vehicles when it detects a traffic jam
Actors:	User, Autopilot
Preconditions:
Postconditions:
Flow:	Autopilot version / The vehicle notices the big amount of vehicles in its way which are all at a halt / The vehicle sends a signal and the location of the traffic jam to nearby vehicles which are moving towards where the vehicle is situated
Alternative Flows:	Manual version / The User notices the traffic jam / The User manually sends a signal and the traffic jam’s location by selecting a setting on the vehicle interface
Exceptions:
Requirements:	REQ-3.2
Test Cases:	TC-7.1.1

ID:	SCE-9
Name:	Weather adaption
Created:	28.11.2020	Last Updated:	28.11.2020
Description:	The sensors detect a weather change and the vehicle adapts its driving profile accordingly.
Actors:	Autopilot
Preconditions:	The vehicle is currently driving on a path to its destination.
Postconditions:
Flow:	Sensors detect snow, ice, a wet road or a dry road / Autopilot reduces the speed and increases its turning radius to prevent slipping
Alternative Flows:
Exceptions:
Requirements:	REQ-8
Test Cases:	TC-8.1.*

ID:	SCE-10
Name:	Emergency corridor
Created:	28.11.2020	Last updated:	28.11.2020
Description:	The vehicles must form an emergency corridor when there’s an emergency vehicle approaching.
Actors:	Autopilot
Preconditions:	An emergency vehicle is seen or heard approaching
Postconditions:	The vehicle should return to its previous position if possible
Flow:	If on the leftmost lane: / An emergency vehicle is heard or seen to be approaching / The vehicle moves as far left as possible
Alternative Flow 1:	If the vehicle is not in the leftmost lane: / 2. The vehicle moves as far right as possible.
Alternative flow 2:	The vehicle can’t move because of obstacles that are in the way
Requirements:	REQ-3, REQ-3.2
Test Cases:	TC-9.1.1